## Slide 1
MCU Driver Porting Note

## Slide 2
atmel_mxt_ts.c : main driver process which contains initialization, reading and parsing information block, message handling and reporting, config updating and so on
atmel_mxt_ts.h : macro and structure definition used for main driver process
debug_info.c : debug output for the driver which need to modify with the specified MCU
mcu_interface.c : config arry, sleep and wait implementation , I2C read and write implementation, interrupt related implementation and coordinate, key reporting implementation
mcu_interface.h : type definition, I2C address definition , definition of the function

## Slide 3
Step 1: Copy the five documents to your MCU code project, you can put them into the new folder of maxtouch.
Step2: Search the key word “Modify Note”, and modify at the position where “Modify Note” was and as the instruction
below the key word. Most of the modification will be occurred in the file of mcu_interface.c.
Step3: After all were modified, you should call mxt_initialize() in your main loop. Then you can build the project and
test with the debug info.
Porting Steps

## Slide 4
Debug tips – information block
1. If the IC is in normal mode and the I2C read function is normal, you will get the correct information through
mxt_read_info_block(). You will see the debug info of all the object information.
Tip1: I2C read will be abnormal if the I2C read function don’t use 16 bit register in the IC or I2C pin don’t have pull-up.
Tip2: The I2C reading reports error if the IC is in bootloader mode because of hardware error.
Tip3: If you get the info of information block crc error, you must check the I2C transfer to make it completely right.

## Slide 5
Debug tips – interrupt and report
2. Please make sure the external interrupt is normal. And then you can get the messages after power on. If the config is
normal, you will get messages when you touch the screen.
Tip1: If the interrupt is abnormal, you should check the level of CHG pin. The CHG should be low after power on and when
there’s message to report in the IC.
Tip2: You should check the I2C read function if the CHG pin is always low. In the normal mode, the CHG pin should be high
after the messages are read by the MCU.

## Slide 6
Debug tips – config update
3. The config update function is very important for maintain the host machine. If there’s no update function, you need to
break the machine to do upgrade. You can add some conditions to judge whether it need to upgrade.
Tip1: I2C write function may be no effect. You can do a easy test to make sure the writing is OK. You should write the
device address, 16bit reg, data together as the datasheet instructed.
Tip2: The config crc get from power on will indicate whether you update successfully.